MPC Controller
Andreas Gotterba
# 1. Edited Files
agotterba_mpc_writeup.pdf	This Document
src/
main.cpp	main program
MPC.h	MPC controller header file
MPC.cpp	MPC controller implementation
Videos
50 mph lap:	https://youtu.be/q0zoL7J5ZWo

# 2. Model Description
## 2.1 State
The state variables are:
x:	The x coordinate of the car
y:	The y coordinate of the car
psi:	The angle the car is pointing
v:	The speed of the car
cte:	The cross track error of the car, relative to the computed (polynomial) centerline
epsi:	The error in the angle of the car, relative to the computed angle of the centerline

Note that all measurements are made relative to the car’s current position. So in the car’s current state, x, y, and psi are all 0. These state variables take on different values for future time-steps, as the model predicts what each of these values will be relative to the car’s current position.
## 2.2 Actuators
The actuators are:
sangle:	The steering angle of the car (processed in radians, and then converted to ‘25	degrees = 1.0’ at the end
acc:	The acceleration (throttle) of the car. The model is ideal (so it really considers	this acceleration), but there is resistance/friction/drag in the simulator.	Thus, when the model targets 50mph, it ends up running at around 48.5 mph.
## 2.3 Update Equations
For each time-step, the model predicts the values of the state variables, based on the previous state and the values of the actuators that were applied. The fundamental equations are:
x[t+1]	=	x[t] + v[t] * cos(psi[t]) * dt
y[t+1]	=	y[t] + v[t] * sin(psi[t]) * dt
psi[t+1]	=	psi[t] - (v[t]/Lf) * sangle[t] * dt
v[t+1]	=	v[t] + acc[t] * dt
cte[t+1]	=	f(x[t]) - y(t) + v[t] * sin(epsi[t]) * dt
epsi[t+1]	=	psi[t] - psides(x[t]) + (v0/Lf) * sangle[t] * dt
Most of the operands are the state and actuators described above; the additional parameters are:

Lf:	The length from the front axle of the car to its center of gravity. Supplied as part of the	starter code, from the result of a controlled simulation.

f(x[t]): this function returns the y coordinate for the centerline of the road at a given x	coordinate (and I use the x coordinate for time t). This could be any means of figuring	out the y coordinate; in this implementation, I’m using the polynomial model from the	waypoints received from the simulator, so I simply evaluate the polynomial at x[t].

psides(x[t]): this function returns the angle of the road’s centerline at a given x coordinate (and	I pass in the x coordinate for time t). This could be any means of finding the angle; in	this implementation, I’m using the polynomial model from the waypoints received from	the simulator; I compute the derivative of the polynomial, then take the arctangent of	that to find the angle.

The actual equations I’m using are in lines 180 through 189 of MPC.cpp. Note that the code is a bit more involved than what I’ve shown here. Instead of the raw update equations, these are implemented as constraints. On its own, the model would think it could pick any value for x[t+1] that it likes. But I’ve already constrained fg[1+param_start+t] to be zero. Therefore, these equations tell it that x[t+1] minus (the equation I wrote above) should be zero, thus constraining the value of x[t+1] that it picks to be equal to the update equation written above.
# 3. Timestep Length and Elapsed Duration

# 4. Polynomial Fitting and MPC Preprocessing

# 5. Latency